## Slide 1
㈜에스비
센터 이전 네트워크 신규 구축 제안서

## Slide 2
CONTENTS
01 _ 개요
02 _ 기술 요약
03 _ 네트워크 구축
04 _ 서버 환경 구축
ETC _ IP 할당 내역 및 소스코드

## Slide 3
01_
개요
1-1 구축 배경 및 목적
02_ 기술 요약
03_ 네트워크 구축
04_ 서버 환경 구축
ETC _
가. 사업명 : (주)에스비 센터 이전 네트워크 신규 구축
나. 일 정 : 2020년 3월 16일(월) ~ 6월 18일(목)
다. 목적
• ㈜에스비의 고성능, 고효율 시스코 네트워크 장비 설치를 통한 차세대 네트워크 시스템 구축
- ㈜에스비 업무를 효율적으로 수용하는 네트워크 인프라 구축
- 차세대 DMZ Zone 과 내부 서버팜 영역 운영의 안정성과 확장성을 보장하는 네트워크 구축
라. 내용
• SB 센터
- EIGRP, NAT 등의 네트워킹 기술을 이용한 네트워크 망 구성
- 이중화와 이더채널을 이용한 안정성 및 효율성 추구
- 서버실1, 2 를 통한 DMZ Zone 영역 구축 예정
- 차세대 내부 서버팜 영역 구축 예정
* 실습 환경 내 Ether-Channel 구현에 제한이 있어 포트 연결을 하나로 수정 후 결과값을 도출하였습니다.

## Slide 4
02_
기술 요약
기술 요약
내부 네트워크 구축
서버 환경 구축
보안 환경 구성
이중화
HSRP를 사용한 Virtual Router를 구현
특정 구간 장애가 발생 시 네트워크서비스를 사용하는 데에 있어 제한 없음
가용성
보안
01_ 개요
03_ 네트워크 구축
04_ 서버 환경 구축
ETC _
AAA권한 등급과 스위치 보안 설정으로 인한 보안 확대
SVI 인터페이스를 구현하여 트래픽 제어를 통한 빠르고 신속한 네트워크 구현

## Slide 5
03_
네트워크 구축
L3 Switch
01_ 개요
02_ 기술 요약
04_ 서버 환경 구축
ETC _
통신 방향
경영지원본부
VLAN 13
마케팅본부
VLAN 14
고객지원본부
VLAN 15
기획관리본부
VLAN 16
서버실 2
VLAN 12
서버실 1
VLAN 11
DSW 1
DSW 2
ASW 6
ASW 5
ASW 4
ASW 3
ASW 2
ASW 1
CORE 1
CORE 2
ISP 2
ISP 1
Internet

## Slide 6
03_
네트워크 구축
01_ 개요
02_ 기술 요약
04_ 서버 환경 구축
ETC _
R .E. A
Network
Cisco 3550 (Switch) | 주요 특징 |  |  | 
 | IOS버전 | C3550 Software Version 12.2 | PoE | 지원하지 않음
 | DRAM | 122880K | GBIC | Giga-stack, CWDM
 | Flash Memory | 8184K | 내장형 RMON | 기록, 경로, 이벤트
 | 고정형 포트 | 10/100포트 24개 | 크기 | 1.75x17.5x14.4
 | 최대 VLAN | 1005 |  | 
 | FEC/GEC | 지원 |  | 
Cisco 2801 (Router) | 주요 특징 |  |  | 
 | IOS버전 | 2800Software Version12.4(22)YB2 | 랙 높이 | 1랙장치(1RU)
 | DRAM | 60416k | 크기 | 437x445x491mm
 | Flash Memory | 5120k | W중량 | 13.7Ib(6kg)
 | 카드 슬롯 | HWIC, WIC, VIC | RPS | 지원하지 않음
 | 콘솔포트 | 1 | 크기 | 13.7Ib(6kg)
 | 하드웨어암호화 | 지원 | AC입력전원 | 100-240VAC
3-1 장비 내역

## Slide 7
03_
네트워크 구축
01_ 개요
02_ 기술 요약
04_ 서버 환경 구축
ETC _
06_ MARKETING
ISP1
ISP2
3-2 구성도 및 기술 (EIGRP)
Core 1
Core 2
EIGRP
100
01_ 개요
02_ 기술 요약
04_ 서버 환경 구축
ETC _
03_
네트워크 구축
1) Ether-Channel을 케이블확장으로 인한 대역폭 증가 및 속도 증가
2) 스위치 장비의 해당 포트 장애 시 대비 위한 이중화 링크 구현
ISP1
Core 1

## Slide 8
3-2 구성도 및 기술 (Ether-Channel)
서버실1
CORE 1
CORE 2
DSW 2
DSW 1
Po 4
Po 4
Po 3
Po 3
CORE 1
DSW 2
DSW 1
CORE 2
01_ 개요
02_ 기술 요약
04_ 서버 환경 구축
ETC _
03_
네트워크 구축
1) Ether-Channel을 케이블확장으로 인한 대역폭 증가 및 속도 증가
2) 스위치 장비의 해당 포트 장애 시 대비 위한 이중화 링크 구현
Core 1 Ether-Channel
Core 2 Ether-Channel

## Slide 9
03_
네트워크 구축
01_ 개요
02_ 기술 요약
04_ 서버 환경 구축
ETC _
06_ MARKETING
3-2 구성도 및 기술 (Ether-Channel)
서버실2
Mail Server
서버실1
Web Server
DNS Server
FTP Server
DSW1
DSW2
서버실1
서버실2
서버실1
서버실2
Po11
Po13
Po12
Po14
01_ 개요
02_ 기술 요약
04_ 서버 환경 구축
ETC _
03_
네트워크 구축
DSW 1 Ether-Channel
DSW 2 Ether-Channel
1) Ether-Channel을 케이블확장으로 인한 대역폭 증가 및 속도 증가
2) 스위치 장비의 해당 포트 장애 시 대비 위한 이중화 링크 구현

## Slide 10
03_
네트워크 구축
01_ 개요
02_ 기술 요약
04_ 서버 환경 구축
ETC _
06_ MARKETING
ISP1
ISP2
3-2 구성도 및 기술 (NAT)
Core 1
Core 2
NAT
NAT
NAT
NAT
F0/1
F0/0
F0/1
F0/0
F0/10
F0/10
01_ 개요
02_ 기술 요약
04_ 서버 환경 구축
ETC _
03_
네트워크 구축
1)사설 IP 대역 을 사용한 여러 네트워크를
공인 IP 대역 과 연결 하기 위해 NAT를 사용
ISP 1 NAT
ISP 2 NAT

## Slide 11
03_
네트워크 구축
01_ 개요
02_ 기술 요약
04_ 서버 환경 구축
ETC _
3-2 구성도 및 기술 (HSRP-1)
Core 2
F0/23-24
ISP1
ISP2
Core 1
DSW 1
DSW 2
F0/0
F0/0
F0/10
F0/10
F0/23-24
F0/19-20
F0/19-20
Virtual Router 5ea
01_ 개요
02_ 기술 요약
04_ 서버 환경 구축
ETC _
03_
네트워크 구축
CISCO 전용 게이트웨이 이중화 프로토콜
하나의 네트워크에 복수의 게이트웨이 사용시, 첫번째 게이트웨이에 장애 발생시
예비 라우터가 게이트웨이로서 동작하도록 구성하는 프로토콜
Core 1 HSRP
Core 2 HSRP

## Slide 12
03_
네트워크 구축
01_ 개요
02_ 기술 요약
04_ 서버 환경 구축
ETC _
3-2 구성도 및 기술 (HSRP-2)
01_ 개요
02_ 기술 요약
04_ 서버 환경 구축
ETC _
03_
네트워크 구축
1) VLAN 12 구간 장애발생 전과 후
Core 1
Core 2
DSW 2
F0/10
F0/24
F0/24
Virtual Router 5ea
장애발생
서버실2
Mail Server
서버실1
DNS&DHCP Server
FTP Server
Po12
Po14
Po13
Po11
F0/10
F0/0
F0/0
F0/19
F0/19
F0/24
F0/24
F0/19
F0/19
WEB Server
DSW 1
장애 발생
BLK -> FWD
통신 방향

## Slide 13
03_
네트워크 구축
01_ 개요
02_ 기술 요약
04_ 서버 환경 구축
3-2 구성도 및 기술 (HSRP-3)
01_ 개요
02_ 기술 요약
04_ 서버 환경 구축
ETC _
03_
네트워크 구축
1) VLAN 13 구간 장애발생 전과 후
Core 1
Core 2
DSW 2
F0/10
F0/24
F0/24
Virtual Router 5ea
장애발생
F0/10
F0/0
F0/0
F0/19
F0/19
F0/24
F0/24
F0/19
F0/19
DSW 1
장애 발생
BLK -> FWD
경영지원본부
VLAN 13
F0/2
F0/1
통신 방향

## Slide 14
03_
네트워크 구축
01_ 개요
02_ 기술 요약
ETC _
4-1 DHCP&DNS SERVER
01_ 개요
02_ 기술 요약
03_ 네트워크 구축
ETC _
04_
서버 환경 구축
각 부서의 IP설정은 PC의 고장으로 인한 수리, 교체에 대한 전산실의 관리대장 작성이 용이하도록 고정 IP설정으로 구현
서버실 IP설정의 경우 작업용 PC의 IP설정을 DHCP로 자동할당 받도록 구현
서버실2
Mail Server
서버실1
Web Server
DHCP&DNS Server
FTP Server
DSW1
DSW2
Po11
Po13
Po12
Po14
작업용 PC
작업용 PC
1. 구성도

## Slide 15
03_
네트워크 구축
01_ 개요
02_ 기술 요약
ETC _
4-1 DHCP&DNS SERVER
01_ 개요
02_ 기술 요약
03_ 네트워크 구축
ETC _
04_
서버 환경 구축
2. IP 할당 범위 설정 및 임대 내역

## Slide 16
03_
네트워크 구축
01_ 개요
02_ 기술 요약
04_ 서버 환경 구축
ETC _
4-1 DHCP&DNS SERVER
01_ 개요
02_ 기술 요약
03_ 네트워크 구축
ETC _
04_
서버 환경 구축
2. IP 할당 범위 설정 및 임대 내역

## Slide 17
03_
네트워크 구축
01_ 개요
02_ 기술 요약
04_ 서버 환경 구축
ETC _
4-1 DHCP&DNS SERVER
01_ 개요
02_ 기술 요약
03_ 네트워크 구축
ETC _
04_
서버 환경 구축
1. DNS 주소 설정, 확인

## Slide 18
03_
네트워크 구축
01_ 개요
02_ 기술 요약
04_ 서버 환경 구축
ETC _
4-2 MAIL SERVER
01_ 개요
02_ 기술 요약
03_ 네트워크 구축
ETC _
04_
서버 환경 구축
서버실2
Mail Server
서버실1
Web Server
DHCP&DNS Server
FTP Server
DSW1
DSW2
Po11
Po13
Po12
Po14
작업용 PC
작업용 PC
1. 구성도 및 전송 확인

## Slide 19
03_
네트워크 구축
01_ 개요
02_ 기술 요약
04_ 서버 환경 구축
ETC _
4-3 FTP SERVER
01_ 개요
02_ 기술 요약
03_ 네트워크 구축
ETC _
04_
서버 환경 구축
1. 서버 구현 및 확인

## Slide 20
03_
네트워크 구축
01_ 개요
02_ 기술 요약
04_ 서버 환경 구축
ETC _
4-4 WEB SERVER
01_ 개요
02_ 기술 요약
03_ 네트워크 구축
ETC _
04_
서버 환경 구축
1. Web 서버 IP 주소 지정 및 문서 우선순위 설정

## Slide 21
03_
네트워크 구축
01_ 개요
02_ 기술 요약
04_ 서버 환경 구축
ETC _
4-4 WEB SERVER
01_ 개요
02_ 기술 요약
03_ 네트워크 구축
ETC _
04_
서버 환경 구축
2. Web 서버 폴더 공유 설정

## Slide 22
03_
네트워크 구축
01_ 개요
02_ 기술 요약
04_ 서버 환경 구축
ETC _
4-4 WEB SERVER
01_ 개요
02_ 기술 요약
03_ 네트워크 구축
ETC _
04_
서버 환경 구축
3. Web 서버 접속 확인

## Slide 23
IP 할당 내역 및 소스코드

## Slide 24
상세구간 | 장비/모델명 | Interface | Ether Channel | 네트워크 | IP Address | VLAN | 비고
ISP1 | Cisco 2801 (Route) | F0/0 | - | 61.42.1.0/24 | 61.42.1.254 | - | 
 |  | F0/1 | - | 192.168.1.0/24 | 192.168.1.131 | - | 
ISP2 |  | F0/0 | - | 61.42.2.0/24 | 61.42.2.254 | - | 
 |  | F0/1 | - | 192.168.1.0/24 | 192.168.1.231 | - | 
CORE1 | Cisco 3550 (Switch) | F0/10 | - | 61.42.1.0/24 | 61.42.1.1 | - | 
 |  | F0/19 | Po4 | - | - | - | Trunk
 |  | F0/24 | Po3 | - | - | - | 
CORE2 |  | F0/10 | - | 61.42.2.0/24 | 61.42.2.1 | - | 
 |  | F0/19 | Po4 | - | - | - | Trunk
 |  | F0/24 | Po3 | - | - | - | 
DSW1 |  | F0/19 | Po4 | - | - | - | Trunk
 |  | F0/24 | Po3 | - | - | - | 
 |  | F0/5 | Po12 | - | - | 11 | 
 |  | F0/6 | Po14 | - | - | 12 | 
 |  | F0/11 | - | - | - | 13 | 
 |  | F0/8 | - | - | - | 14 | 
 |  | F0/9 | - | - | - | 15 | 
 |  | F0/10 | - | - | - | 16 | 

## Slide 25
상세구간 | 장비/모델명 | Interface | Ether Channel | 네트워크 | IP Address | VLAN | 비고
DSW2 | Cisco 3550 (Switch) | F0/19 | Po4 | - | - | - | Trunk
 |  | F0/24 | Po3 | - | - | - | 
 |  | F0/5 | Po11 | - | - | 11 | 
 |  | F0/6 | Po13 | - | - | 12 | 
 |  | F0/11 | - | - | - | 13 | 
 |  | F0/8 | - | - | - | 14 | 
 |  | F0/9 | - | - | - | 15 | 
 |  | F0/10 | - | - | - | 16 | 
ASW1 |  | F0/1 | Po12 | - | - | - | 
 |  | F0/2 | Po11 | - | - | - | 
 |  | F0/3-4, F0/24 | - | 10.1.11.0/24 | - | 11 | 
ASW2 |  | F0/1 | Po14 | - | - | - | 
 |  | F0/2 | Po13 | - | - | - | 
 |  | F0/3-4, F0/24 | - | 10.1.12.0/24 | - | 12 | 
ASW3 |  | F0/1 | - | - | - | - | Trunk
 |  | F0/2 | - | - | - | - | 
 |  | F0/24 | - | 10.1.13.0/24 | - | 13 | Voice Vlan 200

## Slide 26
상세구간 | 장비/모델명 | Interface | Ether Channel | 네트워크 | IP Address | VLAN | 비고
ASW4 | Cisco 3550 (Switch) | F0/1 | - | - | - | - | Trunk
 |  | F0/2 | - | - | - | - | 
 |  | F0/24 | - | 10.1.14.0/24 | - | 14 | Voice Vlan 200
ASW5 |  | F0/1 | - | - | - | - | Trunk
 |  | F0/2 | - | - | - | - | 
 |  | F0/24 | - | 10.1.15.0/24 | - | 15 | Voice Vlan 200
ASW6 |  | F0/1 | - | - | - | - | Trunk
 |  | F0/2 | - | - | - | - | 
 |  | F0/24 | - | 10.1.16.0/24 | - | 16 | Voice Vlan 200

## Slide 27
소스 코드_1
ISP 1 | ISP 2
en conf t hostname ISP1 no ip domain lookup enable secret cisco ! line con 0 logg syn exec-timeout 0 0 password ciscocon login ! line vty 0 4 password ciscovty exit ! int f0/0 ip address 61.42.1.254 255.255.255.0 no sh ! int f0/1 ip address 192.168.1.131 255.255.255.0 no sh ! access-list 10 permit 10.1.0.0 0.0.255.255 access-list 10 permit 192.168.0.0 0.0.255.255 ! ip nat inside source list 10 interface f0/1 overload ! int f0/1 ip nat outside ! int f0/0 ip nat inside ! exit ! router eigrp 100 network 192.168.0.0 0.0.255.255 network 61.42.0.0 0.0.255.255 network 10.1.0.0 0.0.255.255 no auto-summary ! exit ! ip route 0.0.0.0 0.0.0.0 192.168.1.1 ! | en conf t hostname ISP2 no ip domain-lookup enable secret cisco ! line con 0 logg syn exec-timeout 0 0 password ciscocon login ! line vty 0 4 password ciscovty exit ! int f0/0 ip address 61.42.2.254 255.255.255.0 no sh ! int f0/1 ip address 192.168.1.231 255.255.255.0 no sh ! access-list 10 permit 10.1.0.0 0.0.255.255 access-list 10 permit 192.168.0.0 0.0.255.255 ! ip nat inside source list 10 interface f0/1 overload ! int f0/1 ip nat outside ! int f0/0 ip nat inside ! exit ! router eigrp 100 network 192.168.0.0 0.0.255.255 network 61.42.0.0 0.0.255.255 network 10.1.0.0 0.0.255.255 no auto-summary ! exit ! ip route 0.0.0.0 0.0.0.0 192.168.1.1 !

## Slide 28
소스 코드_2
Core 1 (L3 Switch) |  | 
en conf t hostname Core1 no ip domain-lookup enable secret cisco ! line con 0 logg syn exec-timeout 0 0 password ciscocon login ! line vty 0 15 password ciscovty exit ! int vlan 1 ip address 192.168.100.1 255.255.255.0 no shutdown exit ! vtp domain CISCO vtp password cisco1234 exit ! ip routing ! int fa0/19 switchport trunk encapsulation dot1q switchport mode trunk channel-group 4 mode active no sh exit ! int fa0/24 switchport trunk encapsulation dot1q switchport mode trunk channel-group 3 mode active no sh exit ! int port-channel 3 switchport trunk encapsulation dot1q switchport mode trunk ! | int port-channel 4 switchport trunk encapsulation dot1q switchport mode trunk exit ! int vlan 11 ip address 10.1.11.10 255.255.255.0 ip helper-address 10.1.11.222 no shutdown standby 1 ip 10.1.11.254 standby 1 preempt exit ! int vlan 12 ip address 10.1.12.10 255.255.255.0 ip helper-address 10.1.11.222 no shutdown standby 2 ip 10.1.12.254 standby 2 preempt exit ! int vlan 13 ip address 10.1.13.10 255.255.255.0 no shutdown standby 3 ip 10.1.13.254 standby 3 priority 120 standby 3 preempt exit ! int vlan 14 ip address 10.1.14.10 255.255.255.0 no shutdown standby 4 ip 10.1.14.254 standby 4 priority 120 standby 4 preempt exit ! int vlan 15 ip address 10.1.15.10 255.255.255.0 no shutdown standby 5 ip 10.1.15.254 standby 5 priority 120 standby 5 preempt exit ! | int vlan 16 ip address 10.1.16.10 255.255.255.0 no shutdown standby 6 ip 10.1.16.254 standby 6 priority 120 standby 6 preempt exit ! int fa0/10 no switchport ip address 61.42.1.1 255.255.255.0 no shutdown exit ! ip route 0.0.0.0 0.0.0.0 61.42.1.254 ! router eigrp 100 network 61.42.0.0 0.0.255.255 network 10.1.0.0 0.0.255.255 no auto-summary ! exit ! spanning-tree vlan 13-16 priority 4096 spanning-tree vlan 11-12 priority 40960 ! spanning-tree mode rapid-pvst !

## Slide 29
소스 코드_3
Core 2 (L3 Switch) |  | 
en conf t hostname Core2 no ip domain-lookup enable secret cisco ! line con 0 logg syn exec-timeout 0 0 password ciscocon login ! line vty 0 15 password ciscovty exit ! int vlan 1 ip address 192.168.100.2 255.255.255.0 no shutdown exit ! vtp domain CISCO vtp password cisco1234 ! exit ! ip routing ! int fa0/19 switchport trunk encapsulation dot1q switchport mode trunk channel-group 4 mode active no sh exit ! int fa0/24 switchport trunk encapsulation dot1q switchport mode trunk channel-group 3 mode active no sh exit ! int port-channel 3 switchport trunk encapsulation dot1q switchport mode trunk ! | int port-channel 4 switchport trunk encapsulation dot1q switchport mode trunk exit ! int vlan 11 ip address 10.1.11.11 255.255.255.0 no shutdown standby 1 ip 10.1.11.254 standby 1 priority 120 standby 1 preempt ! int vlan 12 ip address 10.1.12.11 255.255.255.0 no shutdown standby 2 ip 10.1.12.254 standby 2 priority 120 standby 2 preempt ! int vlan 13 ip address 10.1.13.11 255.255.255.0 no shutdown standby 3 ip 10.1.13.254 standby 3 preempt ! int vlan 14 ip address 10.1.14.11 255.255.255.0 no shutdown standby 4 ip 10.1.14.254 standby 4 preempt ! int vlan 15 ip address 10.1.15.11 255.255.255.0 no shutdown standby 5 ip 10.1.15.254 standby 5 preempt ! int vlan 16 ip address 10.1.16.11 255.255.255.0 no shutdown standby 6 ip 10.1.16.254 standby 6 preempt ! | int fa0/10 no switchport ip address 61.42.2.1 255.255.255.0 no shutdown exit ! ip route 0.0.0.0 0.0.0.0 61.42.2.254 ! router eigrp 100 network 61.42.0.0 0.0.255.255 network 10.1.0.0 0.0.255.255 no auto-summary ! exit ! spanning-tree vlan 13-16 priority 40960 spanning-tree vlan 11-12 priority 4096 ! spanning-tree mode rapid-pvst !

## Slide 30
소스 코드_4
DSW 1 | 
en conf t hostname DSW1 no ip domain-lookup enable secret cisco ! line con 0 logg syn exec-timeout 0 0 password ciscocon login ! line vty 0 15 password ciscovty exit ! vtp domain CISCO vtp password cisco1234 ! exit ! ip routing int range f0/1-11 switchport trunk encapsulation dot1q switchport mode trunk exit ! int f0/20 switchport trunk encapsulation dot1q switchport mode trunk channel-group 4 mode active exit ! int f0/24 switchport trunk encapsulation dot1q switchport mode trunk channel-group 3 mode active exit ! | int f0/5 channel-group 12 mode active exit ! int f0/6 channel-group 14 mode active exit ! int port-channel 3 switchport trunk encapsulation dot1q switchport mode trunk exit ! int port-channel 4 switchport trunk encapsulation dot1q switchport mode trunk exit ! int port-channel 12 switchport trunk encapsulation dot1q switchport mode trunk exit ! int port-channel 14 switchport trunk encapsulation dot1q switchport mode trunk exit ! int vlan 1 ip address 192.168.100.3 255.255.255.0 no shutdown exit ! spanning-tree vlan 11-12 priority 16384 spanning-tree vlan 13-16 priority 8192 ! spanning-tree mode rapid-pvst !

## Slide 31
소스 코드_5
DSW 2 | 
en conf t hostname DSW2 no ip domain-lookup enable secret cisco ! line con 0 logg syn exec-timeout 0 0 password ciscocon login ! line vty 0 15 password ciscovty exit ! vtp domain CISCO vtp password cisco1234 ! exit ! ip routing int range f0/1-11 switchport trunk encapsulation dot1q switchport mode trunk exit ! int f0/20 switchport trunk encapsulation dot1q switchport mode trunk channel-group 4 mode active exit ! int f0/24 switchport trunk encapsulation dot1q switchport mode trunk channel-group 3 mode active exit ! int f0/5 channel-group 11 mode active exit ! | int f0/6 channel-group 13 mode active exit ! int port-channel 3 switchport trunk encapsulation dot1q switchport mode trunk exit ! int port-channel 4 switchport trunk encapsulation dot1q switchport mode trunk exit ! int port-channel 11 switchport trunk encapsulation dot1q switchport mode trunk exit ! int port-channel 13 switchport trunk encapsulation dot1q switchport mode trunk exit ! int vlan 1 ip address 192.168.100.4 255.255.255.0 no shutdown exit ! spanning-tree vlan 11-12 priority 8192 spanning-tree vlan 13-16 priority 12288 ! spanning-tree mode rapid-pvst !

## Slide 32
소스 코드_6
ASW 1 | ASW 2 | ASW 3
en conf t hostname ASW1 no ip domain-lookup enable secret cisco ! line con 0 logg syn exec-timeout 0 0 password ciscocon login ! line vty 0 15 password ciscovty exit ! vtp domain CISCO vtp password cisco1234 ! vlan 11 name VLAN_11 exit ! int range f0/1-2 switchport trunk encapsulation dot1q switchport mode trunk exit ! int f0/1 channel-group 12 mode active exit ! int f0/2 channel-group 11 mode active exit ! int range f0/3-4 switchport access vlan 11 switchport mode access spanning-tree portfast ! int range f0/23-24 switchport access vlan 11 switchport mode access spanning-tree portfast exit ! int vlan 1 ip address 192.168.100.5 255.255.255.0 no shutdown ! spanning-tree vlan 11 priority 12288 ! | en conf t hostname ASW1 no ip domain-lookup enable secret cisco ! line con 0 logg syn exec-timeout 0 0 password ciscocon login ! line vty 0 15 password ciscovty exit ! vtp domain CISCO vtp password cisco1234 ! vlan 12 name VLAN_12 exit ! int range f0/1-2 switchport trunk encapsulation dot1q switchport mode trunk exit ! int f0/1 channel-group 14 mode active exit ! int f0/2 channel-group 13 mode active exit ! int range f0/3-4 switchport access vlan 12 switchport mode access spanning-tree portfast ! int range f0/23-24 switchport access vlan 12 switchport mode access spanning-tree portfast exit ! int vlan 1 ip address 192.168.100.6 255.255.255.0 no shutdown ! spanning-tree vlan 12 priority 12288 ! | en conf t hostname ASW3 no ip domain-lookup enable secret cisco ! line con 0 logg syn exec-timeout 0 0 password ciscocon login ! line vty 0 15 password ciscovty exit ! vtp domain CISCO vtp password cisco1234 ! vlan 13 name VLAN_13 exit ! int range f0/1-2 switchport trunk encapsulation dot1q switchport mode trunk exit ! int f0/24 switchport trunk encapsulation dot1q switchport mode trunk switchport trunk native vlan 13 switchport voice vlan 200 spanning-tree portfast trunk exit ! int vlan 1 ip address 192.168.100.7 255.255.255.0 no shutdown ! spanning-tree vlan 13 priority 32768 !

## Slide 33
소스 코드_7
ASW 4 | ASW 5 | ASW 6
en conf t hostname ASW4 no ip domain-lookup enable secret cisco ! line con 0 logg syn exec-timeout 0 0 password ciscocon login ! line vty 0 15 password ciscovty exit ! vtp domain CISCO vtp password cisco1234 ! vlan 14 name VLAN_14 exit ! int range f0/1-2 switchport trunk encapsulation dot1q switchport mode trunk exit ! int f0/24 switchport trunk encapsulation dot1q switchport mode trunk switchport trunk native vlan 14 switchport voice vlan 200 spanning-tree portfast trunk exit ! int vlan 1 ip address 192.168.100.8 255.255.255.0 no shutdown ! spanning-tree vlan 14 priority 32768 !! | en conf t hostname ASW5 no ip domain-lookup enable secret cisco ! line con 0 logg syn exec-timeout 0 0 password ciscocon login ! line vty 0 15 password ciscovty exit ! vtp domain CISCO vtp password cisco1234 ! vlan 15 name VLAN_15 exit ! int range f0/1-2 switchport trunk encapsulation dot1q switchport mode trunk exit ! int f0/24 switchport trunk encapsulation dot1q switchport mode trunk switchport trunk native vlan 15 switchport voice vlan 200 spanning-tree portfast trunk exit ! int vlan 1 ip address 192.168.100.9 255.255.255.0 no shutdown ! spanning-tree vlan 15 priority 32780 ! | en conf t hostname ASW6 no ip domain-lookup enable secret cisco ! line con 0 logg syn exec-timeout 0 0 password ciscocon login ! line vty 0 15 password ciscovty exit ! vtp domain CISCO vtp password cisco1234 ! vlan 16 name VLAN_16 exit ! int range f0/1-2 switchport trunk encapsulation dot1q switchport mode trunk exit ! int f0/24 switchport trunk encapsulation dot1q switchport mode trunk switchport trunk native vlan 16 switchport voice vlan 200 spanning-tree portfast trunk exit ! int vlan 1 ip address 192.168.100.10 255.255.255.0 no shutdown ! spanning-tree vlan 16 priority 32780 !

## Slide 34
감사합니다
THANK YOU